Product Descriptions

MetraTherm 1 Infrared Thermometer

Infrared Thermometer with Laser Sight

for contactless measurement of surface temperature

Applications:

Temperature measurement at large distances, and thus at a safe distance from potential danger zones

Electrical troubleshooting, repairs and maintenance work in the automotive industry and in air conditioners

Scientific experiments, manufacturing processes in the field of semiconductor technology

Contacts in electrical control cabinets, food monitoring and processing

Features:

Infrared temperature measuring range: -50 to 1000° C (-58 to 1832° F)

Exact positioning with laser sighting (can be activated if desired)

High distance ratio (E:M): 50:1

Emissivity adjustable from 0.1 to 1.00 in steps of 0.01

Additional measuring option with type K thermocouple

Selectable unit of measure: °C or °F

Individual and continuous measurements, 10 memory locations for individual measurements

Storage of currently measured temperature, lowest and highest temperature or maximum temperature difference DT

Illuminated LCD panel

Alarm function: acoustic signal if selectable limit values are exceeded or fallen short of

USB port for data transmission to a PC

PC software for displaying and recording measured values (data logger function) on included CD ROM

The included PC software makes the following functions possible:

PC Display and Recording Program (data logger)

Display of currently measured infrared temperature values with date and time

Adjust the sampling interval for recording measured values

Record measured values to a text file which can be exported to Microsoft‚ Excel for analysis

Included:

METRATHERM 1, 9 V battery, screw-on carrying strap, type K thermocouple, USB adapter cable for communication between the measuring instrument and the PC, CD ROM with PC display and recording program (data logger), operating instructions in English and German

Product Code: M680A